## Slide 1: ECE 721 Overview
Spring’23
Prof. Rotenberg

## Slide 2: Performance Strategies
Application Class | Nature of Parallelism | Architecture Approach
sequential programs | Instruction-Level Parallelism (ILP) irregular and fine-grained | general-purpose superscalar or VLIW speculation is key theme
data-parallel programs | Data-Level Parallelism (DLP) regular and fine-grained | vector, SIMD, SIMT (GPGPU)
thread-parallel programs | Thread-Level Parallelism (TLP) regular and coarse-grained | parallel computers, multi-core
ECE 721
ECE 786
ECE 706
ECE 506
ECE 563

## Slide 3: The Big Five ILP Techniques (ECE 463/563 Review)
Pipelining
  Overlap instructions for higher throughput
Caches, prefetching
  Bridge processor-memory speed gap
Branch prediction
  Remove control dependencies for effective pipelining
Out-of-order execution
  Tolerate long-latency instructions (multi-cycle instructions, cache-missed loads) by fetching and executing future independent instructions while dependent instructions wait
  Expose adequate instruction-level parallelism to supply the parallel execution lanes of a superscalar processor (next bullet)
Superscalar
  Exceed scalar (1 instr./cycle) performance via multiple-instruction issue (N instr./cycle)

## Slide 4: ILP Scaling in Commercial Processors
Processor Generation | Pipeline Depth (fetch to execute) | Issue Width | In-flight Instructions
Pentium | 5 | 1 instr. | ~5
Pentium-III | 10 | 3 µ-ops | ~40
Pentium-IV | 20 | 3 µ-ops | 126
IBM Power4 | 12 | 5 instr. | 200
IBM Power8 |  | 10 (issue) 8 (retire) | 224

## Slide 5
ECE 463/563: Reorder Buffer; ECE 721: Active List
Load Queue
Store Queue
Issue Queue, a.k.a. Reservation Stations, a.k.a. Scheduler
ECE 463/563: ARF+Reorder Buffer; ECE 721: Physical Register File
ECE 463/563: ARF+Reorder Buffer; ECE 721: Physical Register File

## Slide 6
Apple’s CPUs still pretty much remain a black box design given that the company doesn’t disclose any details, and the only publicly available resources on the matter date back to LLVM patches in the A7 Cyclone era, which very much aren’t relevant anymore to today’s designs. While we don’t have the official means and information as to how Apple’s CPU work, that doesn’t mean we cannot figure out certain aspects of the design. Through our own in-house tests as well as third party microbenchmarks (A special credit due for @Veedrac’s microarchitecturometer test suite), we can however unveil some of the details of Apple’s designs. The following disclosures are estimated based on testing the behavior of the latest Apple A14 SoC inside of the iPhone 12 Pro: Apple's Firestorm CPU Core: Even Bigger & Wider
…
Source: https://www.anandtech.com/show/16226/apple-silicon-m1-a14-deep-dive/2
“Apple's Humongous CPU Microarchitecture”
Disclaimer:

## Slide 7: ECE 721 Topics
Two styles of OOO
  563: ARF+ROB
  721: PRF (Physical Register File)
  0.5 lecture contrasting the two
  4.5 lectures on PRF management
Handling loads and stores
  Review from 563
  Some additional depth

## Slide 8: ECE 721 Topics (cont.)
How to scale the processor window to thousands of instructions?
  More latency tolerance
  Expose more ILP
  Checkpoint Processing and Recovery (CPR)
    Large virtual window (e.g., 2K in-flight instructions) with smaller PRF
    Hierarchical SQ
Project 4 (final project): CPR

## Slide 9: ECE 721 Topics (cont.)
Canonical superscalar pipeline
  Example superscalar fetch stage
  Example superscalar rename stage
  Challenges to scaling superscalar width
Scaling superscalar width
  Trace cache
  Trace processor

## Slide 10: ECE 721 Topics (cont.)
Try to improve gshare accuracy with the TAGE predictor
Dealing with delinquent (hard-to-predict) branches
  Major IPC bottleneck in some benchmarks
  Don’t predict the branch: predication and skipper
  Predict branch and exploit control independence for selective recovery
  Improve branch prediction via branch pre-execution
  About multipath execution: it is a hard-sell (see me for my perspective)
TAGE paper to be posted
A control-independence paper will be posted
Skipper paper to be posted
A branch pre-execution paper will be posted

## Slide 11: ECE 721 Topics (cont.)
Value prediction
  Try to increase ILP by breaking true data dependencies
  Improve load latency tolerance
  Alternative to larger windows
Simultaneous Multithreading (SMT)
  Intel’s implementation is called “hyperthreading”
  Multiple threads share the superscalar processor
  Increase utilization of the superscalar processor
  More so-called ILP via TLP

## Slide 12: Style 1 (ECE 563)
writeback
execute

## Slide 13: Style 2 (ECE 721)
Issue
Queue
(IQ)
Function
Units (FUs)
Physical
RF
Map
Active List
tail
head
Free list
Shadow
Maps
Arch.
Map
exception
recovery
misp.
recovery
branch
rename
retire
I$
branch
predictor
decode, rename, dispatch
instruction fetch
OOO issue
execution
writeback
register read

## Slide 14: Project Framework and Projects 1-4
721sim (C++)
  Cycle-level, execution-driven, execute-at-execute simulator of a superscalar processor
  Actually two simulators: a functional-only simulator checks retired values of the functional-and-timing simulator
Project 1
  ILP limit study (identify performance bottlenecks and opportunities in real benchmarks)
  No coding. Use 721sim executable.
  Learn how to run benchmark “SimPoints” on 721sim
Projects 2 and 3
  Project 2: Implement centerpiece Renamer module (PRF management), plug into 721sim
  Project 3: 721sim source code revealed, implement missing pieces that interface with the Renamer module
  Projects 2 and 3 are training ground (reinforce concepts and get familiar with 721sim for Project 4)
Project 4
  The current plan is for the whole class to implement CPR in 721sim
  CPR’s PRF management, hierarchical SQ, and coarse-grain recovery
  Address 721sim infrastructure aspects and CPR microarchitecture aspects
  Validate performance across many configurations and multiple benchmarks (for grading and for gaining insights about CPR performance)