## Slide 1: ARF+ROB vs. PRF
ECE 721
Prof. Eric Rotenberg

## Slide 2: ECE 563 Style (ARF+ROB)
physical register file = ARF + ROB values
Commit by moving ROB value at head into ARF
Recovery
  Wait until exception/misprediction reaches head
  T=H
  Clear all “v” bits
r0
r31
rob0
rob127
commit
v
ROB tag
H
T
r5
r6
r0
r31
r5
r6
rob15
rob77
r5=
r5=
1
ROB values
ROB ready bits
Rename Map Table (RMT)
Architectural Register File (ARF)
77
0
-
Reorder Buffer (ROB)

## Slide 3: ECE 563 Style (ARF+ROB)
Rename
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
v = RMT[r].v
tag = RMT[r].ROB_tag
Read ARF and ROB, set up operand for Issue Queue:
  if (v==0) {
  ready = 1;
  tag_or_value = ARF[r];
  }
  else {
  ready = ROB[tag].ready;
  tag_or_value =
  (ready ? ROB[tag].value : tag);
  }
IQ[x].src1.ready = ready
IQ[x].src1.tag_or_value = tag_or_value
Retire
What’s shown in this picture: renaming an instruction’s first source operand, denoted with architectural register specifier “r”, and setting up its state in the Issue Queue (IQ).

## Slide 4: ECE 563 Style (ARF+ROB)
Rename
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
“Register Read” stage before “Issue” stage
  Can’t be after
  If value is available at time of renaming, must grab it and capture it in Issue Queue (IQ)
  If IQ only kept pointer to value (ROB tag), value could move from ROB to ARF before instruction issues and then the pointer is stale
Retire

## Slide 5: ECE 721 Style (PRF)
Committing and freeing registers does not involve data movement
Recovery conceptually similar, but restoring RMT not a simple flash-clear of bits
p0
p159
Phys. Reg. Tag
r0
r31
r5
r6
PRF ready bits
Rename Map Table (RMT)
Physical Register File (PRF)
p99
p13
p25
p4
PRF values

## Slide 6: ECE 721 Style (PRF)
Rename
Decode
Fetch
Register Read
Dispatch
Issue
Execute
Writeback
tag = RMT[r]
IQ[x].src1.ready = PRF[tag].ready
IQ[x].src1.tag = tag
value = PRF[tag].value
“Register Read” stage after “Issue” stage
Issue Queue (IQ)
  No values, just tags
Retire
What’s shown in this picture: renaming an instruction’s first source operand, denoted with architectural register specifier “r”, and setting up its state in the Issue Queue (IQ).