## Slide 1: Physical Register File Management: Renaming
ECE 721
Prof. Eric Rotenberg

## Slide 2: Logical registers
Logical registers
  Also called architectural registers
  Registers defined in the instruction-set architecture (ISA)
  Program registers (registers you see in the program binary)
Example: Alpha ISA
  32 logical integer registers (r0-r31)
  32 logical floating-point registers

## Slide 3: Physical registers
Physical registers
  Hardware registers
Example: Alpha 21264 microarchitecture
  80 physical integer registers (p0-p79)
  72 physical floating-point registers

## Slide 4: Renaming
Renaming
  Assign a unique physical register to a logical register
Number of physical registers > number of logical registers
  Multiple definitions of a logical register are each assigned a unique physical register

## Slide 5: Structures (required)
Physical register file
Rename map table
Free list
  List of unused registers in physical register file
Active list
  Active instruction: Instruction that has been dispatched but not yet retired
  Active list: List of all active instructions in program order
  Equivalent to the Reorder Buffer (ROB)

## Slide 6: Structures (optional)
Architectural map table
  Recovery from exceptions and mispredictions (branch, load, etc.)
  Restore rename map table to committed state
Shadow map tables
  Recovery from branch mispredictions
  Restore rename map table to what it was just after the branch

## Slide 7: Side notes
Alternate names for map tables
  Rename map table: frontend map table
  Architectural map table: backend map table
Optional structures
  Architectural map table is optional
  Shadow map tables are optional
  Whether or not these exist depends on recovery strategies. Active list alone can be used for recovery. Recovery strategies affect contents of active list and existence of the architectural and shadow map tables. More on this later…

## Slide 8: Renaming
Rename logical source registers
  Obtain mappings from rename map table
Rename logical destination register
  Pop a free physical register from the free list
  Assign the physical register to the logical destination register
  Update rename map table to reflect the new mapping

## Slide 9: Renaming example
load r1, 16(r2)
load r1, 20(r2)
sub r4, r1, #1
add r3, r1, #1

## Slide 10: Renaming example (cont.)
Rename Map Table (before)
load r1, 16(r2)
r0 | p10
r1 | p8
r2 | p11
r3 | p33
r4 | p46
… | 
r31 | p2
p67 | p19 | p27 | p28 | … | p5 | …
p11
head
tail
p67
Free List (before)
Rename Map Table (after)
r0 | p10
r1 | p67
r2 | p11
r3 | p33
r4 | p46
… | 
r31 | p2
p67 | p19 | p27 | p28 | … | p5 | …
head
tail
Free List (after)
load p67, 16(p11)

## Slide 11: Renaming example (cont.)
Rename Map Table (before)
r0 | p10
r1 | p67
r2 | p11
r3 | p33
r4 | p46
… | 
r31 | p2
p67 | p19 | p27 | p28 | … | p5 | …
p67
head
tail
p19
Free List (before)
Rename Map Table (after)
r0 | p10
r1 | p67
r2 | p11
r3 | p19
r4 | p46
… | 
r31 | p2
p67 | p19 | p27 | p28 | … | p5 | …
head
tail
Free List (after)
add r3, r1, #1
add p19, p67, #1

## Slide 12: Renaming example (cont.)
Rename Map Table (before)
r0 | p10
r1 | p67
r2 | p11
r3 | p19
r4 | p46
… | 
r31 | p2
p67 | p19 | p27 | p28 | … | p5 | …
p11
head
tail
p27
Free List (before)
Rename Map Table (after)
r0 | p10
r1 | p27
r2 | p11
r3 | p19
r4 | p46
… | 
r31 | p2
p67 | p19 | p27 | p28 | … | p5 | …
head
tail
Free List (after)
load r1, 20(r2)
load p27, 20(p11)

## Slide 13: Renaming example (cont.)
Rename Map Table (before)
r0 | p10
r1 | p27
r2 | p11
r3 | p19
r4 | p46
… | 
r31 | p2
p67 | p19 | p27 | p28 | … | p5 | …
p27
head
tail
p28
Free List (before)
Rename Map Table (after)
r0 | p10
r1 | p27
r2 | p11
r3 | p19
r4 | p28
… | 
r31 | p2
p67 | p19 | p27 | p28 | … | p5 | …
head
tail
Free List (after)
sub r4, r1, #1
sub p28, p27, #1

## Slide 14: Renaming example (cont.)
load r1, 16(r2)
load r1, 20(r2)
sub r4, r1, #1
add r3, r1, #1
load p67, 16(p11)
add p19, p67, #1
load p27, 20(p11)
sub p28, p27, #1
load p67, 16(p11)
add p19, p67, #1
load p27, 20(p11)
sub p28, p27, #1