## Slide 1: Committing and freeing registers
Active list
  Controls committing and freeing of physical registers
  A single action does both: Committing a register means the previously-committed register can be freed (its value is no longer needed)

## Slide 2: Two Different Approaches
Approach #1:
  Architectural Map Table
    Whereas Rename Map Table contains most recent versions of logical registers, Arch. Map Table contains committed versions of logical registers
Approach #2:
  No Architectural Map Table

## Slide 3: Approach #1
load r1, 16(r2)
load r1, 20(r2)
sub r4, r1, #1
add r3, r1, #1
load p67, 16(p11)
add p19, p67, #1
load p27, 20(p11)
sub p28, p27, #1
We’ll use our on-going example:

## Slide 4: Active List (with AMT)
Entry | logical dest. | physical dest.: current mapping | exc. | comp. | PC
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
… |  |  |  |  | 
ACTIVE LIST
head
tail
AMT
r0 | p10
r1 | p8
r2 | p11
r3 | p33
r4 | p46
… | 
r31 | p2
RMT
r0 | p10
r1 | p8
r2 | p11
r3 | p33
r4 | p46
… | 
r31 | p2
AMT: committed versions (“trailing edge” of core)
RMT: most recent versions (“leading edge” of core)

## Slide 5: Active List (with AMT)
Entry | logical dest. | physical dest.: current mapping | exc. | comp. | PC
1 |  |  |  |  | 
2 |  |  |  |  | 
3 | r1 | p67 | 0 | 0 | A
4 |  |  |  |  | 
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
… |  |  |  |  | 
ACTIVE LIST
head
tail
r0 | p10
r1 | p8
r2 | p11
r3 | p33
r4 | p46
… | 
r31 | p2
r0 | p10
r1 | p67
r2 | p11
r3 | p33
r4 | p46
… | 
r31 | p2
AMT
RMT

## Slide 6: Active List (with AMT)
Entry | logical dest. | physical dest.: current mapping | exc. | comp. | PC
1 |  |  |  |  | 
2 |  |  |  |  | 
3 | r1 | p67 | 0 | 0 | A
4 | r3 | p19 | 0 | 0 | B
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
… |  |  |  |  | 
ACTIVE LIST
head
tail
r0 | p10
r1 | p8
r2 | p11
r3 | p33
r4 | p46
… | 
r31 | p2
r0 | p10
r1 | p67
r2 | p11
r3 | p19
r4 | p46
… | 
r31 | p2
AMT
RMT

## Slide 7: Active List (with AMT)
Entry | logical dest. | physical dest.: current mapping | exc. | comp. | PC
1 |  |  |  |  | 
2 |  |  |  |  | 
3 | r1 | p67 | 0 | 0 | A
4 | r3 | p19 | 0 | 0 | B
5 | r1 | p27 | 0 | 0 | C
6 |  |  |  |  | 
7 |  |  |  |  | 
… |  |  |  |  | 
ACTIVE LIST
head
tail
r0 | p10
r1 | p8
r2 | p11
r3 | p33
r4 | p46
… | 
r31 | p2
r0 | p10
r1 | p27
r2 | p11
r3 | p19
r4 | p46
… | 
r31 | p2
AMT
RMT

## Slide 8: Active List (with AMT)
Entry | logical dest. | physical dest.: current mapping | exc. | comp. | PC
1 |  |  |  |  | 
2 |  |  |  |  | 
3 | r1 | p67 | 0 | 0 | A
4 | r3 | p19 | 0 | 0 | B
5 | r1 | p27 | 0 | 0 | C
6 | r4 | p28 | 0 | 0 | D
7 |  |  |  |  | 
… |  |  |  |  | 
ACTIVE LIST
head
tail
r0 | p10
r1 | p8
r2 | p11
r3 | p33
r4 | p46
… | 
r31 | p2
r0 | p10
r1 | p27
r2 | p11
r3 | p19
r4 | p28
… | 
r31 | p2
AMT
RMT

## Slide 9: Committing and freeing registers
Entry | logical dest. | physical dest.: current mapping | exc. | comp. | PC
1 |  |  |  |  | 
2 |  |  |  |  | 
3 | r1 | p67 | 0 | 1 | A
4 | r3 | p19 | 0 | 0 | B
5 | r1 | p27 | 0 | 0 | C
6 | r4 | p28 | 0 | 0 | D
7 |  |  |  |  | 
… |  |  |  |  | 
ACTIVE LIST
head
tail
r0 | p10
r1 | p8
r2 | p11
r3 | p33
r4 | p46
… | 
r31 | p2
r0 | p10
r1 | p27
r2 | p11
r3 | p19
r4 | p28
… | 
r31 | p2
AMT
RMT
p67
p8
Free List
tail
“commit”
“free”

## Slide 10: Active List Operation
Dispatch:
  Reserve entry at tail, write the instruction’s logical and physical destination register specifiers, increment tail pointer
  “Current mapping”: instruction’s physical destination register specifier

## Slide 11: Active List Operation (cont.)
Retire:
  Wait for head instruction to complete
  Index Arch. Map Table using the head instruction’s logical destination register specifier
    Free the “previous mapping” that is contained in the Arch. Map Table: push it onto the free list. Since we are about to commit a new version, the old committed version is no longer needed for possible recovery.
    Physical register indicated by “current mapping” is committed by updating the Arch. Map Table with the current mapping.
  Advance head pointer

## Slide 12: Handling Exceptions
Set exception bit in active list
When posted exception reaches head of active list:
  Flush active list: Set tail pointer equal to head pointer
  Flush pipeline: Squash all instructions in frontend stages, issue queues, FUs, etc.
  Restore rename map table to committed state: Copy architectural map table to rename map table
  Restore free list: Push mappings of all instructions after the offending one back onto the free list
  Save PC of offending instr. (gotten from head of active list)
    E.g., MIPS ISA defines EPC register where handler will return to
    EPC = AL[al_head].PC
  Trap to the exception handler
    PC = address of exception handler

## Slide 13: Implementation Challenges (1)
Squashing instructions in pipeline
  Global squash signal may be cycle time bottleneck
  Extending to multiple cycles provides some relief
  Still a routing bottleneck (physical design)
Alternative: wait for all in-flight instructions to “drain” from pipeline (i.e., wait for all of them to complete)
  No global squash signal
  Wait extra cycles as pipeline drains. Can overlap some cycles with restoring RMT from AMT if it takes multiple cycles to copy

## Slide 14: Implementation Challenges (2)
Restoring Rename Map Table from Arch. Map Table
Solution 1: “flash copy”
  Fast (one or a few cycles)
  Requires either (a) an exotic SRAM design, or (b) synthesizing to a flip-flop-based design (more area)
Solution 2: serial copy
  Conventional SRAM design
  Speed limited by read and write ports of the two map tables

## Slide 15: Determining number of ports for renaming structures
Free List
Active List
? W
RMT
? R
? R
rename logical destination registers
rename logical source registers
? R
AMT
? W
? W
? R
? W
T
H
H
T
Example:
4-way superscalar i.e., 4 instr. in rename bundle and 4 instr. in retire bundle
Assume maximum of 2 source registers and 1 destination register for an instruction
RENAME
RETIRE

## Slide 16: Aside: head/tail phase bits for circular FIFOs
For a circular FIFO, H==T can mean either empty or full
Distinguish empty vs. full using phase bits
  A pointer’s phase bit toggles when it wraps around
  Example:
  empty = ((H==T) && (H_phase == T_phase));
    H and T wrapped around same number of times.
  full = ((H==T) && (H_phase != T_phase));
    T wrapped around one more time than H did.
T++; // increment tail pointer
if (T == FIFO_size) { // wrap around scenario
T = 0; // force wrap around
T_phase = !T_phase; // toggle phase bit
}
uint64_t FIFO_size;
uint64_t H, T;
bool H_phase, T_phase;

## Slide 17: Aside: head/tail phase bits for circular FIFOs
H(0)
T(0)
key:
H(H_phase)
T(T_phase)
a
H(0)
T(0)
a
b
H(0)
T(0)
a
b
c
H(0)
T(0)
a
b
c
d
H(0)
T(1)
empty
full
a
b
c
d
H(0)
T(1)
pop a
e
b
c
d
H(0)
T(1)
push e
push a
push b
push c
push d
full
e
b
c
d
H(0)
T(1)
pop b
e
b
c
d
H(0)
T(1)
pop c
e
b
c
d
H(1)
T(1)
pop d
e
b
c
d
H(1)
T(1)
pop e
empty

## Slide 18: Implementation Challenges (3)
Two options for restoring free list
  Slow and complex:
    Scan active list between head and tail, push each instruction’s current mapping back onto free list
    Fortunately there is a more clever way…
  Fast and simple:
    Observation about free list contents:
      Between H and T: List of free physical registers
      Between T and H: List of physical registers allocated to instructions between active list H and T
        Popping mappings from free list merely advances its head pointer but does not destroy contents
    Restore free list simply by rolling back head pointer to tail pointer (bulk-undo the speculative pops) and noting that the free list is full
      head = tail
      head_phase = !(tail_phase)

## Slide 19
Architectural Map Table
KEY:
speculative registers, free
speculative registers, allocated to active instructions
committed registers
…
Active List
Free List
tail(1)
head(0)
initial state: pipeline empty
r1
Note:
Free List size (max # free registers for speculation) = PRF size - # logical registers (committed state can’t be free)
Active List size >= Free List size AL typically larger than FL because not all active instructions have logical destination registers
…
p19
p67
p28
p27
…
…
tail(0)
head(0)
empty
full
p8

## Slide 20
Architectural Map Table
KEY:
speculative registers, free
speculative registers, allocated to active instructions
committed registers
…
Active List
Free List
tail(1)
r1
…
p19
p67
p28
p27
…
…
head(0)
r3:p19
r1: p67
r1:p27
branch
store
r4:p28
p8
head(0)
after dispatching instructions
tail(0)

## Slide 21
Architectural Map Table
KEY:
speculative registers, free
speculative registers, allocated to active instructions
committed registers
…
Active List
Free List
tail(1)
r1
…
p19
p67
p28
p27
…
…
head(0)
r3:p19
r1: p67
r1:p27
branch
store
r4:p28
p8
head(0)
after retiring head instruction
tail(0)
p67
p8

## Slide 22
Architectural Map Table
KEY:
speculative registers, free
speculative registers, allocated to active instructions
committed registers
…
Active List
Free List
tail(1)
r1
…
p19
p8
p28
p27
…
…
head(0)
r3:p19
r1: p67
r1:p27
branch
store
r4:p28
p67
head(0)
exception at head of Active List
tail(0)
completed =1 exception=1

## Slide 23
Architectural Map Table
KEY:
speculative registers, free
speculative registers, allocated to active instructions
committed registers
…
Active List
Free List
tail(1)
r1
…
p19
p8
p28
p27
…
…
head(0)
r3:p19
r1: p67
r1:p27
branch
store
r4:p28
p67
head(0)
after recovery
tail(0)
empty
full
Free List exception recovery logic:
head = tail
head_phase = !tail_phase
Active List exception recovery logic:
tail = head
tail_phase = head_phase

## Slide 24: Common Question from Students
Why not unify Active List and Free List?
Conceivable, but there is a drawback (1) or it’s not possible (2):
  Unifying them wastes physical registers because not all active instructions need a physical register. If separate, Active List may be larger than Free List. (FYI: 563’s ARF+ROB wastes ROB registers, e.g., stores and branches in ROB.)
  Not possible for Approach #2 (coming up) because Active List has previous mappings instead of current mappings.

## Slide 25: Approach #2
load r1, 16(r2)
load r1, 20(r2)
sub r4, r1, #1
add r3, r1, #1
load p67, 16(p11)
add p19, p67, #1
load p27, 20(p11)
sub p28, p27, #1
We’ll use our on-going example:

## Slide 26: Active List (without AMT)
Entry | logical dest. | physical dest.: previous mapping | exc. | comp. | PC
1 |  |  |  |  | 
2 |  |  |  |  | 
3 | r1 | p8 | 0 | 0 | A
4 | r3 | p33 | 0 | 0 | B
5 | r1 | p67 | 0 | 0 | C
6 | r4 | p46 | 0 | 0 | D
7 |  |  |  |  | 
… |  |  |  |  | 
ACTIVE LIST
head
tail
By keeping the previous mapping, that was overwritten in the RMT by the instruction’s current mapping, the Active List serves as an “undo log”, i.e., we can rollback the RMT to the committed state (i.e., what the RMT was when the pipeline was empty) without an explicit AMT.

## Slide 27
Logical Dest. | Previous mapping
r1 | p8
Active List (after)
H
T
Logical Dest. | Previous mapping
r1 | p8
r3 | p33
Active List (after)
H
T
Logical Dest. | Previous mapping
r1 | p8
r3 | p33
r1 | p67
Active List (after)
H
T
Logical Dest. | Previous mapping
r1 | p8
r3 | p33
r1 | p67
r4 | p46
Active List (after)
H
T

## Slide 28: Committing and freeing registers
Entry | logical dest. | physical dest.: previous mapping | exc. | comp. | PC
1 |  |  |  |  | 
2 |  |  |  |  | 
3 | r1 | p8 | 0 | 1 | A
4 | r3 | p33 | 0 | 0 | B
5 | r1 | p67 | 0 | 0 | C
6 | r4 | p46 | 0 | 0 | D
7 |  |  |  |  | 
… |  |  |  |  | 
ACTIVE LIST
head
tail
p8
Free List
tail
“free”
“commit”:
This action implicitly commits the head instruction’s version of r1 (p67).

## Slide 29: Active List Operation
Rename:
  Before updating the Rename Map Table with a new mapping for an instruction’s logical destination register, read out the previous mapping for that logical destination register
  This requires an extra read port for the logical destination register of an instruction:
    phys. source reg. 1 = RMT[logical source reg. 1] // RMT read port
    phys. source reg. 2 = RMT[logical source reg. 2] // RMT read port
    phys. dest. reg. = pop new mapping from free list
    RMT[logical dest. reg.] = phys. dest. reg. // RMT write port
Approach #1 (with Arch. Map Table)
    phys. source reg. 1 = RMT[logical source reg. 1] // RMT read port
    phys. source reg. 2 = RMT[logical source reg. 2] // RMT read port
    previous mapping = RMT[logical dest. reg.] // extra RMT read port
    phys. dest. reg. = pop new mapping from free list
    RMT[logical dest. reg.] = phys. dest. reg. // RMT write port
Approach #2 (without Arch. Map Table)

## Slide 30: Active List Operation (cont.)
Dispatch:
  Reserve entry at tail, write the instruction’s logical destination register specifier and the previous mapping of that logical register, increment tail pointer
Retire:
  Wait for head instruction to complete
  Push its previous mapping onto the free list. This has two implicit effects:
    Frees the prior committed version of the instruction’s logical dest. register
    Commits the instruction’s physical dest. register
  Advance head pointer

## Slide 31: Handling Exceptions
Set exception bit in active list
When posted exception reaches head of active list:
  Flush pipeline: Squash all instructions in frontend stages, issue queues, FUs, etc.
  Restore rename map table to committed state: Scan the active list backward from tail to head, restore previous mappings into rename map table
  Restore free list: Either:
    Easy: Restore head pointer as before (head=tail, head_phase=!tail_phase)
    More complicated than needed: While restoring the rename map table, “undone” current mappings are pushed back onto free list
  Save PC of offending instr. (gotten from head of active list)
  Trap to the exception handler

## Slide 32
Logical Dest. | Previous mapping
r1 | p8
r3 | p33
r1 | p67
r4 | p46
Active List
H
T
Rename Map Table
r0 | p10
r1 | p27
r2 | p11
r3 | p19
r4 | p28
… | 
r31 | p2
Logical Dest. | Previous mapping
r1 | p8
r3 | p33
r1 | p67
r4 | p46
H
T
r0 | p10
r1 | p27
r2 | p11
r3 | p19
r4 | p28
… | 
r31 | p2
Initial: renamed four instr.
After commit of oldest instr.
r1:p8 freed, implicitly committed r1:p67
Suppose second instr., now at head (H), posted an exception. Restore prev. mappings from T to H from AL to RMT.
Logical Dest. | Previous mapping
r1 | p8
r3 | p33
r1 | p67
r4 | p46
H
T
r0 | p10
r1 | p27
r2 | p11
r3 | p19
r4 | p28 p46
… | 
r31 | p2
Logical Dest. | Previous mapping
r1 | p8
r3 | p33
r1 | p67
r4 | p46
H
T
r0 | p10
r1 | p27 p67
r2 | p11
r3 | p19
r4 | p46
… | 
r31 | p2
Logical Dest. | Previous mapping
r1 | p8
r3 | p33
r1 | p67
r4 | p46
H
T
r0 | p10
r1 | p67
r2 | p11
r3 | p19 p33
r4 | p46
… | 
r31 | p2
Original RMT (before instr. sequence)
Final RMT (after recovery)
r0 | p10
r1 | p67
r2 | p11
r3 | p33
r4 | p46
… | 
r31 | p2
r0 | p10
r1 | p8
r2 | p11
r3 | p33
r4 | p46
… | 
r31 | p2

## Slide 33: Branch Misprediction Recovery Approaches
These approaches wait for the mispredicted branch to reach the head of the active list (like an exception), before initiating recovery.
Handle like exception using approach #1
Handle like exception using approach #2
These approaches initiate recovery as soon as the misprediction is discovered (as soon as the branch instruction executes), from the middle of the active list.
Forward walk active list
Backward walk active list
Shadow Map Tables

## Slide 34: Branch Misprediction Recovery Approaches 3, 4, & 5
Free List: For all three approaches, checkpoint the free list head pointer and head phase bit after* the branch is renamed. Restoring the checkpointed free list head pointer and head phase bit associated with the mispredicted branch causes mappings of instructions after the branch to be freed in bulk.
  (* Some branch opcodes may have a logical destination register. If the branch was mispredicted, note that the branch itself is correct.)
Rename Map Table: Need to restore the RMT to what it was just after renaming the branch. The three approaches differ in this aspect. See following slides.

## Slide 35: Approach #3: Forward walk active list
Same structures as Approach #1
  Active List contains current mappings, which are used to update an Architectural Map Table
When misprediction is detected:
  Restore RMT from AMT right away (either flash copy or serial copy)
  Fast-forward the RMT to just after the branch in the active list, by walking the active list from head to branch (inclusive) and incrementally updating the RMT with the current mappings in the active list

## Slide 36: Approach #3 (cont.)
Approach #3 and Approach #1 seem to be equal but opposite
  Approach #1: Waits for branch to reach head of active list, then copy AMT to RMT
  Approach #3: Immediately copy AMT to RMT, then walk forward from head to branch
So how is Approach #3 better?
  Approach #1 is delayed by the time to execute and retire all instructions prior to the branch. E.g., what if there is an L2-cache-missed load stalling retirement for 100s of cycles?
  Approach #3’s recovery latency only depends on the number of instructions prior to the branch, not the time to execute those instructions

## Slide 37: Approach #4: Backward walk active list
Same structures as Approach #2
  Active List contains previous mappings; no AMT
When misprediction is detected:
  Roll-back the RMT to just after the branch in the active list, by walking the active list from tail to the entry just after the branch (inclusive) and incrementally restoring the RMT with the previous mappings in the active list

## Slide 38: Approach #5: Shadow Map Tables
Checkpoint (create a copy of) the RMT after renaming a branch
  Checkpoint RMT after branch is renamed, since state of RMT at this point reflects renaming all instructions up to and including the branch, and none after
  Let’s call a checkpointed copy of the RMT a Shadow Map Table
When misprediction is detected:
  Restore RMT from the mispredicted branch’s Shadow Map Table

## Slide 39: Clarification about branch checkpoints
Approaches #3, #4, and #5 all use branch checkpoints
Contents of branch checkpoint (at a minimum)
  Checkpointed free list head pointer and head phase bit: approaches #3, #4, and #5
  Checkpointed GBM (see Project 2): approaches #3, #4, and #5
  Checkpointed RMT, a.k.a., Shadow Map Table: approach #5 only

## Slide 40: Recovery from branch mispredictions, for immediate recovery (#3, #4, #5)
Recovery steps for approaches #3, #4, and #5
  Pipeline
    Instruction fetch unit
      Set PC to the correct target of the branch
      Repair the global branch history register of the branch predictor (if applicable)
    Frontend stages: fetch, decode, rename, dispatch
      Squash all instructions in the frontend stages since these are by definition after the resolved branch
    Backend stages: schedule, register read, execute, writeback
      Selectively squash only those instructions in the backend stages that come after the mispredicted branch in program order
      Each instruction inherits a branch dependence bit vector in the rename stage, with one bit per unresolved branch, indicating which unresolved branches are before the instruction in program order

## Slide 41: Recovery from branch mispredictions, for immediate recovery (#3, #4, #5)
Recovery steps (cont.)
  Renaming machinery
    Active list
      Restore active list tail to the entry just after the mispredicted branch (must restore tail pointer and tail phase bit)
    Free list
      Restore free list head to the checkpointed free list head (head pointer and head phase bit)
    Rename map table
      #3: forward walk; #4: backward walk; #5: shadow map
    Reclaim the checkpoints of the mispredicted branch and all later branches. Also see next slide.

## Slide 42: See Project 2 for efficient branch checkpoint management
Global branch mask (GBM)
  Maintained in the Rename Stage
  Allocating a free bit in the GBM for a just-renamed branch gives it a unique branch ID (bit position in the GBM) which is also its index into an array of checkpoints
    bit in the GBM  branch ID  index into array of checkpoints
  A renamed instruction knows which unresolved branches are prior to it in program order (whichever branch bits are set in the GBM when the instruction is renamed). Used for selective squashing of instructions in the backend stages.
  Checkpointing the GBM in branch checkpoints, and later restoring it, yields implicit reclamation of checkpoints of branches after the mispredicted branch
Confused? Implement Project 2 (and 3) and it will help.

## Slide 43
commit-and-free registers: Approach #1:
Active List has current mappings
AMT
commit-and-free registers: Approach #2:
Active List has previous mappings
no AMT
Exception recovery approach #1:
Wait until offending instr. is at AL head, don’t retire offending instruction
Full squash pipeline
RMT = AMT
fl_head = fl_tail, fl_head_phase = !fl_tail_phase
al_tail = al_head, al_tail_phase = al_head_phase
Save offending PC in EPC register, etc.
Fetch PC = PC of exception handler
Branch misprediction recovery approach #1:
Wait until misp. branch is at AL head, retire branch
Full squash pipeline
RMT = AMT
fl_head = fl_tail, fl_head_phase = !fl_tail_phase
al_tail = al_head, al_tail_phase = al_head_phase
Fetch PC = correct target of branch
Branch misprediction recovery approach #3 (forward walk):
Initiate misp. recovery immediately
Full squash frontend, selective squash backend
RMT = AMT, forward walk AL from head to br. (inclusive)
Restore free list head and phase from checkpoint
Restore active list tail and phase to entry after branch
Fetch PC = correct target of branch
Branch misprediction recovery approach #5 (shadow maps):
Initiate misp. recovery immediately
Full squash frontend, selective squash backend
Restore RMT from checkpoint
Restore free list head and phase from checkpoint
Restore active list tail and phase to entry after branch
Fetch PC = correct target of branch
Exception recovery approach #2:
Wait until offending instr. is at AL head, don’t retire offending instruction
Full squash pipeline
RMT: backward walk AL from tail to head, restore prev. mappings
fl_head = fl_tail, fl_head_phase = !fl_tail_phase
al_tail = al_head, al_tail_phase = al_head_phase
Save offending PC in EPC register, etc.
Fetch PC = PC of exception handler
Branch misprediction recovery approach #2:
Wait until misp. branch is at AL head, retire branch
Full squash pipeline
RMT: backward walk AL from tail to head, restore prev. mappings
fl_head = fl_tail, fl_head_phase = !fl_tail_phase
al_tail = al_head, al_tail_phase = al_head_phase
Fetch PC = correct target of branch
Branch misprediction recovery approach #4 (backward walk):
Initiate misp. recovery immediately
Full squash frontend, selective squash backend
RMT: backward walk AL from tail to br. (exclusive), restore prev. mappings
Restore free list head and phase from checkpoint
Restore active list tail and phase to entry after branch
Fetch PC = correct target of branch

## Slide 44: Modern Superscalar Microarchitecture
Issue
Queue
(IQ)
Function
Units (FUs)
Physical
RF
tail
head
Shadow
Maps
exception
recovery
misp.
rec.
rename
fetch
decode
rename
dispatch
Free List
Active List
retire
AMT
RMT
head
tail
schedule
execute
register read
writeback
complete
PRF ready bits
clr
set
wakeup
GBM