## Slide 1: Synchronizing Producers and Consumers
There are two parts to synchronizing producers and consumers of registers
  Renaming: Unambiguously link producers and consumers via unique physical register tags
    Already covered this topic of renaming, committing-and-freeing, and recovery of the associated structures (RMT, Free List, Active List).
  Dynamic scheduling: Understand readiness of source operands and issue instructions only when all their source operands are ready.
    Facilitated by two structures: PRF ready bit array and IQ

## Slide 2: Dynamic Scheduling
Physical Register File ready bits
  Used to initialize ready bits of source operands of instructions when they get dispatched into the IQ
  One ready bit per physical register
  Location in pipeline
    NOT located with Physical Register File
    Physically located near the Dispatch and Schedule Stages
Issue Queue (IQ)
  Wait for producers to wakeup non-ready source operands in the IQ

## Slide 3: Operation
Dispatch stage
  Read the PRF ready bits corresponding to the instruction’s source physical registers, to initialize the ready bits of the instruction’s source operands when it is dispatched into the IQ.
  If the instruction has a destination register, it clears the PRF ready bit corresponding to its destination physical register.
Schedule (Issue) stage
  When an instruction with a destination register issues, it sets the PRF ready bit corresponding to its destination physical register and asserts its tag (physical register number) on an IQ wakeup port to wake up any matching non-ready source operands.

## Slide 4
ready bit
source tag
ready bit
source tag
IQ CAM (wakeup array)
IQ RAM (payload)
other payload fields
dest. tag
PRF ready bit array
Instruction’s payload:
destination physical tag
source physical tags
decoded opcode
immediate value
AL index
LQ and SQ indices
branch ID
branch mask
etc.
…
select
logic

## Slide 5
ready bit
source tag
ready bit
source tag
IQ CAM (wakeup array)
IQ RAM (payload)
other payload fields
dest. tag
…
0
…
1
…
…
p99
Dispatch Stage:
PRF ready bit array
p10:
p22:
p99:
1
0
0
dst: p22
src1: p10 (ready=1)
src2: p99 (ready=0)
select
logic

## Slide 6
ready bit
source tag
ready bit
source tag
IQ CAM (wakeup array)
IQ RAM (payload)
other payload fields
dest. tag
1
p10
0
p99
…
p22
0
…
1
…
…
p99
PRF ready bit array
p10:
p22:
p99:
1
0
0
select
logic

## Slide 7
ready bit
source tag
ready bit
source tag
IQ CAM (wakeup array)
IQ RAM (payload)
other payload fields
dest. tag
1
p10
0
p99
…
p22
1
…
1
…
…
p99
PRF ready bit array
p10:
p22:
p99:
1
0
0
select
logic
req.
grant

## Slide 8
ready bit
source tag
ready bit
source tag
IQ CAM (wakeup array)
IQ RAM (payload)
other payload fields
dest. tag
1
p10
1
p99
…
p22
…
p99
PRF ready bit array
p10:
p22:
p99:
1
0
1
select
logic
issue
==
==
wakeup port
a.k.a. CAM read port a.k.a. CAM match port
p99
req.
grant

## Slide 9
ready bit
source tag
ready bit
source tag
IQ CAM (wakeup array)
IQ RAM (payload)
other payload fields
dest. tag
…
p22
PRF ready bit array
p10:
p22:
p99:
1
1
1
select
logic
issue
wakeup port
a.k.a. CAM read port a.k.a. CAM match port
p22

## Slide 10: Wakeup Timing
Execute dependent instructions in consecutive cycles for high performance
  Need to wakeup dependent instructions before data is produced
  Separate tag and data broadcast
IS
RR
EX
WB
IS
RR
EX
WB
DATA BYPASS
TAG
Key:
IS = Schedule Stage
RR = Register Read Stage
EX = Execute Stage
WB = Writeback Stage

## Slide 11: Wakeup Timing (cont.)

## Slide 12: Wakeup Timing (cont.)
Producer instruction delays broadcasting its destination tag based solely on its execution latency
  1-cycle execution latency: broadcast tag 1 cycle after issuing
  2-cycle execution latency: broadcast tag 2 cycles after issuing
  etc.
Delay mechanism is implemented using a shift register
  An Execution Lane has a dedicated shift register
    Input to shift register: the issuing instruction’s destination tag
    Output of shift register: tied to dedicated wakeup port
  Depth of shift register = the Execution Lane’s fixed execution latency