## Slide 1: Sizing Structures
Fixed relations
  Relation of free list size to phys. reg. file size
  Relation of (maximum) phys. reg. file size to active list size
  RMT and AMT (if AMT exists)
Empirical (simulation-based)
  Active list, LQ/SQ, IQ, branch checkpoints

## Slide 2: 1. Free List Size w.r.t. Phys. Reg. File Size
Committed registers can’t be free
Suppose all speculative registers are free (i.e., pipeline empty)
free list size = phys. reg. file size – # logical registers
# speculative registers
# committed registers
# logical registers in ISA
Physical Register File
Free List

## Slide 3: 2. Phys. Reg. File Size w.r.t. Active List Size
# physical registers = # committed registers + # speculative registers
# committed registers = # logical registers
# speculative registers
  What if each active (speculative) instruction has a destination register?
  Upper bound: # speculative registers = active list size
  (maximum) # physical registers = # logical registers + active list size
  Could have fewer than this, because some instructions (stores, most branches) don’t have a destination register
    # physical registers = # logical registers + active list size - x
    x = # entries in active list that don’t have a dest. reg., on average (empirical)

## Slide 4: 3. RMT and AMT
Map table dimensions
  # entries = # logical registers
  # bits per entry = # bits in a physical register tag = ⌈log2(# physical registers)⌉

## Slide 5: 4. Window size
Active list is overall window into dynamic instruction stream
  Instructions between dispatch and retire
Load queue and store queue
  Load and store instructions between dispatch and retire
Issue queue is dynamic scheduling window
  Instructions between dispatch and issue
# branch checkpoints depends on number of unresolved branches
  Branches between rename and writeback
These must be empirically determined because they depend on nature of ILP in programs and target fetch/issue width of processor (N)
  Greater N requires larger inspection scope for finding more independent instructions that can issue in parallel
  Inspection scope also depends on data dependencies, interleaving of dependent/independent instructions, and latencies (cache misses, etc.)

## Slide 6: Window sizing
Short answer
  All resources must be large enough to not stall the fetch stage*
  Implies IPC = N instr./cycle for N-way superscalar
*… which means retire isn’t stalled: resources are large enough to ensure that, despite execution latencies and data-dependent instructions, each N-wide retire bundle is wholly completed by the time the Active List head pointer reaches it.
Active List
H(0)
T(1)
1
1
1
1
1
0
1
1
0
1
0
1
0
1
1
0
1
0
0
1
0
0
0
0
0
0
0
0s/1s: completed bits
e.g.: 4-wide superscalar
full
Retire
Dispatch

## Slide 7: Sizing Structures
N
Physical Register
File
Free List
data dependencies, cache misses, etc., in typical programs
LQ/SQ
IQ
branch checkpoints
Active List
# physical registers = # logical registers + active list size - x
free list size = phys. reg. file size – # logical registers
empirical
depends on factors above
size these “commensurately” (see next slide)

## Slide 8: Sizing Structures (cont.)
in-order allocation (dispatch for IQ, rename for br. chkpts)
OOO reclamation (issue for IQ, writeback for br. chkpts)
in-order allocation (dispatch)
in-order reclamation (retire)
Active List
LQ
SQ
H
T
H
T
H
T
IQ
branch
checkpoints
All instructions use the AL and IQ.
Each instruction is allocated an AL entry and an IQ entry at dispatch.
Each instruction leaves the IQ OOO (when all its source operands are ready).
Each instruction leaves the AL in-order (after all older instr. have retired).
Thus, each instruction spends less time in the IQ than in the AL.
Thus, to size the AL and IQ commensurately, IQ size < AL size.
“Commensurate”: size all structures so that no one structure is the bottleneck, rather, all are equally the bottleneck.